## Slide 1
CENG-232 Logic Design
Lecture 1
Introduction, Digital Logic & Circuits

## Slide 2: Which one?

## Slide 3: Which one?

## Slide 4: This class is about “Digital Systems”
They are everywhere
  They make life easier, more enjoyable
The most famous digital system is
  A general purpose computer
  It has a memory unit, central processing unit and input/output units
  Programmable: same device, many different purposes
At the end of this class, you will be able to
  Design and implement digital systems at various levels of abstraction
Why?
  To make others’ lives easier and more enjoyable some day..
Page 4
232 - Logic Design

## Slide 5: This class is about
Electronics (Transistors)
Digital Circuits
  Combinational (Gates)
  Sequential (Adder, etc.)
Timing
  Signals, Speed, Delay
Physical vs. Logical
Parallelism
Notes: Not a course on transistor physics and transistor circuits. Although, we will look at these to better understand the primitive elements for digital circuits.

## Slide 6: Introduction
What is a digital system?
How it differs from an analog system?
Why are digital systems important?
Basic types of digital systems: combinational and sequential
Specification and implementation of digital systems
Analysis and design of digital systems
Design process and CAD tools
Page 6
232 - Logic Design

## Slide 7: What is Digital?
Digital Systems
  inputs and outputs come from a set of finite number of discrete values
Analog Systems
  inputs and outputs come from a continuous (infinite) set
Example: digital vs. analog scale for measuring weights
Main uses of digital systems:
  Information processing
  Transmission (communication)
  Storage
  Many forms of "information"
Page 7
232 - Logic Design

## Slide 8: Signals and Systems
Page 8
232 - Logic Design

## Slide 9: Why are Digital Systems important?
1) Well suited for both numerical and nonnumerical information processing
2) We can use a general-purpose system for information processing
  a computer
  eliminate the need for having a different system for each task
3) Digital representation:
  Finite number of values in the digital signal can be represented by a vector of signals with just two values (binary signals)
  When all signals are binary we can have simple devices to process binary signals:
    just switches with two states: open and closed
Page 9
232 - Logic Design

## Slide 10: Why Digital?
4) Digital signals quite insensitive to variations of component parameter values
Page 10
232 - Logic Design

## Slide 12: Why Digital?
5) Numerical digital systems can be made more accurate by simply increasing the number of digits used in the representation.
  720p vs 1080p
  12:30 vs 12:30:47
6) Phenomenal advances of microelectronics technology:
  Possible to fabricate (with low cost) extremely complex digital systems that are small, fast and cheap
  Digital systems built as integrated circuits (IC) composed of a large number of very simple devices
Page 12
232 - Logic Design

## Slide 13: Why Digital?
7) Different implementations of systems which trade-off speed and amount of hardware
Example:
  add two integers represented by six decimal digits
Page 13
232 - Logic Design

## Slide 14: Mixed Analog/Digital Systems
Page 14
232 - Logic Design
Notes: There are limits to digital techniques:
  The analog nature of the world requires a time consuming conversion process:
      Convert the physical variable to an electrical signal (analog).
      Convert the analog signal to digital form.
      Process (operate on) the digital information.
      Convert the digital output back to real-world analog form.

## Slide 15: Example of Digitization Benefit

## Slide 16: Ways of digitization
How can we represent binary information?
  CPU
  Hard Disk
  CDs

## Slide 17: Combinational and sequential systems
Digital systems - two classes:
Combinational systems
  z(t) = F(x(t))
  no memory, the output does not depend on previous inputs
Sequential systems
  z(t) = F(x(0; t))
  x(0; t): input sequence from time 0 to time t
  z(t) depends also on previous inputs - the system has memory
Page 17
232 - Logic Design

## Slide 18: Combinational and sequential systems
Page 18
232 - Logic Design

## Slide 19: Example: Combinational System
Input x(t) with values from the set of letters (upper and lower case)
Input y(t) with values 0 and 1
The function:
  change x(t) to opposite case when y(t) = 1
  leave it unchanged when y(t) = 0
An input-output pair:
Page 19
232 - Logic Design

## Slide 20: Example: Sequential System
Input x with values 0,1, or 2
Output z with values 0 or 1
An input-output pair:
Page 20
232 - Logic Design

## Slide 21: Logic Example
Schematic
Representation
HI
0
0
1
1
LO
0
1
0
1
Pump
0
1
0
x
Drain
0
0
1
x
Tank level is OK
Low level, pump more in
High level, drain some out
Inputs cannot occur
Truth Table
Representation
HI
LO
Pump
Drain
Notes: A circuit controlling the level of fluid in a tank
  inputs are:
    HI - 1 if fluid level is too high, 0 otherwise
    LO - 1 if fluid level is too low, 0 otherwise
  outputs are:
    Pump - 1 to pump fluid into tank, 0 for pump off
    Drain - 1 to open tank drain, 0 for drain closed
  input to output relationship is described by a truth table

## Slide 22: Timing Diagrams
Timing Diagram for X and Y (input), Z (output)
Actually, there is a delay at each new rising/falling pulse, but not shown here! (will be discussed later)
X
Y
Z
X
Y
Z
Notes: Timing diagrams show how inputs and outputs for a logic circuit change in time
For given input timing diagrams, we can draw the output timing diagrams for a given combinational circuit.
Consider the following XOR circuit with 2 inputs:

## Slide 23: Analysis / Design
Analysis
Specification
(function and other
characteristics)
Implementation
(network of modules)
Design
WHAT
HOW
Notes: The study of any system involves its specification and implementation.
The specifications refers to a description of its function and of other characteristics required for its use, such as speed technology and power consumption.
Specification is related to what the system does without reference to how it performs the operation.
A specification is should be as complete as possible, all required details should be there and nothing more.
It should be formal in the sense that its interpretation is unambigious.

## Slide 24: Specification and Implementation
The specification of a system describes its function.
Objective:
  to use the system as a component in more complex systems; and
  to serve as the basis for the implementation of the system by a network of simpler components.
Page 24
232 - Logic Design

## Slide 25: Specification
Can be done at different levels
  high-level
  binary-level
  algorithmic-level
For different types of systems:
  Spec. of combinational systems: Chapter 4
  Spec. of sequential systems: Chapter 5
  Spec. of algorithmic systems: Chapter 6, 8
Page 25
232 - Logic Design

## Slide 26: Implementation
How the system is constructed from simpler components
In digital systems, implementation is
  a digital network consists of the interconnection of modules
Several levels depending on the complexity of the primitive modules
  from very simple gates to complex processors
Physical level: interconnection of electronic elements
  Transistors, resistors
Different methods for different types
  Combinational systems: At gate and module levels
  Sequential systems
  Algorithmic systems
Hierarchical implementation
Page 26
232 - Logic Design

## Slide 27: Implementation Levels
Page 27
232 - Logic Design
Notes:  There are two basic approaches to system design
◦ Top-Down: start at the top system level and decompose into ever simpler subsystems and components
◦ Bottoms-Up: start with known low-level building blocks and put them together into increasing complex functions
 Ideally either should work; however, in practice neither method does
Helps control complexity -
  by hiding details and reducing the total number of things to handle at any time.
Modulalizes the design -
  divide and conquer
  simplifies implementation and debugging
Top-Down Design
  Starts at the top (root) and works down by successive refinement.
Bottom-up Design
  Starts at the leaves & puts pieces together to build up the design.
Which is better?
  In practice both are needed & used.
    Need top-down divide and conquer to handle the complexity.
    Need bottom-up because in a well designed system, the structure is influence by what primitves are available.

## Slide 28: Analysis / Design
Analysis
Specification
(function and other
characteristics)
Implementation
(network of modules)
Design
  get specification from an implementation
  obtain an implementation that satisfies the specification

## Slide 29: Structured Analysis and Design
Analysis:
  get specification from an implementation
Design:
  obtain an implementation that satisfies the specification
Use of multilevel approach necessary
The top-down and bottom-up approaches
  There exists no systematic procedures to achieve the optimal
A combination of the two approaches
Page 29
232 - Logic Design

## Slide 30: Levels: module, logical, physical
Page 30
232 - Logic Design

## Slide 31: Computer-Aided Design Tools
Design of digital systems an involved and laborious process
Various computer-aided design (CAD) tools available
Main types of CAD tools support the main phases of digital design:
  description (specification),
  design (synthesis) including various optimizations to reduce cost and improve performance, and
  checking of the design with respect to its specification.
The design phases typically require several passes
Page 31
232 - Logic Design

## Slide 32: CAD
Description of digital systems for design purposes
  At a high-level, use hardware-description language (HDL)
  At the binary level, use HDLs to describe the system structure
  Editors used to produce HDL programs
  Graphical forms - logic diagrams also used for structure
Page 32
232 - Logic Design

## Slide 33: uVHDL Description
USE WORK.ALL;
ENTITY sample_system IS
PORT (xin: IN BIT_VECTOR;
z : OUT BIT_VECTOR;
clk: IN BIT );
END sample_system;
ARCHITECTURE structural OF sample_system IS
SIGNAL xreg, yreg, addout: BIT_VECTOR(7 DOWNTO 0);
BEGIN
RX: ENTITY BitReg8 PORT MAP(xin,xreg,clk);
RY: ENTITY BitReg8 PORT MAP(addout,yreg,clk);
ADD: ENTITY Adder PORT MAP(xreg,yreg,addout);
z <= addout;
END structural;
Page 33
232 - Logic Design

## Slide 34: CAD
Synthesis and optimization tools
  Semi-automated
Simulation tools generate behavior of a system for given input
  Logic simulation
  Timing simulation
Page 34
232 - Logic Design

## Slide 35: Design Trade-offs
You can improve on one at the expense of worsening one or both of the others.
These tradeoffs exist at every level in the system design - every sub-piece and component.
Design Specification -
  Functional Description.
  Performance, cost, power constraints.
As a designer you must make the tradeoffs necessary to achieve the function within the constraints.

## Slide 36: Examples
Computer
  Designed to maximize performance.
  "Optimized for speed”
Handheld calculator
  Usually designed to minimize cost.
  “Optimized for low cost”
  Of course, low cost comes at the expense of speed
Digital watch
  Designed to minimize power. Single battery must last for years.
  Low power operation comes at the expense of:
    lower speed
    higher cost

## Slide 37: Assignment
Read Chapter 1
Optional: Read Appendix A of the book

## Slide 38: Quiz
You already know one of the most complex digital systems
What is the simplest digital communication system ever built?

## Slide 39
Transistors
https://www.youtube.com/watch?v=MVAqfj9RTPA