## Slide 1
CENG-232 Logic Design
Lecture 2
Boolean Algebra & Logic Gates

## Slide 2: Overview
Boolean Algebra
Switching Algebra
Algebraic Minimization
Standard forms
Karnaugh Map Minimization
Other logic operators
IC families and characteristics
Read Chapters 1 & 2
Optional: Read Appendix A of the book

## Slide 3
The principles of logical thinking have been understood since the Hellenic era (c. 500- 300 BC)
George Boole in 1854 showed how to systemize these principles and express them in equations
  Boolean logic or Boolean algebra
A deductive mathematical system
  A set of elements
  A set of operators
  A number of unproved axioms or postulates
Postulates
  Form the basic assumptions from which it is possible to deduce the rules, theorems and properties of the system
Boolean Algebra
Notes: Algebra: the reunion of broken parts
George Boole (1815-1864) developed Boolean logic
The principles of logical thinking have been understood (and occasionally used) since the Hellenic era.
Boole’s contribution was to show how to systemize these principles and express them in equations (called Boolean logic or Boolean algebra).

## Slide 4
Based on Boolean Algebra
Developed by Claude Shannon in 1938 to represent the properties of bistable electrical switching circuits
  showed how to use Boolean algebra as the basis for switching technology
  systemized logical thinking for computer and communication systems, both for the design and programming of the systems and their applications.
Formal way to describe logic statements and determine truth of statements
Only has two-values domain (0 and 1)
Huntington’s Postulates (1904) define underlying assumptions
Switching Algebra
Notes: Claude Shannon (1916-2001) showed how to use Boolean algebra as the basis for switching technology.
This contribution systemized logical thinking for computer and communication systems, both for the design and programming of the systems and their applications.

## Slide 5
Switching Or Boolean Algebra
Defined by
  A set of elements B = [0,1]
  Two binary operators + and .
    the rules of these operations
  Huntington Postulates
Two-valued Boolean Algebra
  With only two elements
Switching Algebra
Notes: Claude Shannon (1916-2001) showed how to use Boolean algebra as the basis for switching technology.
This contribution systemized logical thinking for computer and communication systems, both for the design and programming of the systems and their applications.

## Slide 6: Huntington’s Postulates
1. Closure
  If X and Y are in set (0,1) then operations X+Y and X· Y are also in set (0,1)
2. Identity Element
  X + 0 = X X · 1 = X
3. Commutativity
  X + Y = Y + X X· Y = Y· X

## Slide 7: Huntington’s Postulates (cont.)
4. Distributive
  X · (Y + Z) = (X · Y) + (X · Z)
  X + (Y · Z) = (X + Y) · (X + Z)
5. Complement
  For every element X, there exists an element X’ such that
  X + X’ = 1
  X · X’ = 0
6. There exists at least two elements x, y such that x ≠ y

## Slide 8: Huntington’s Postulates (cont.)
Duality Principle:
  X + 0 = X X · 1 = X
  X + Y = Y + X X· Y = Y· X
  X · (Y + Z) = (X · Y) + (X · Z) X + (Y · Z) = (X + Y) · (X + Z)
  X + X’ = 1 X · X’ = 0
Note that for each property, one form is the dual of the other;
(0’s to 1’s, 1’s to 0’s, ·’s to +’s, +’s to ·’s)

## Slide 9: Switching Algebra Operations - NOT
Result of postulate 5
Unary complement or inversion operation
Usually shown as overbar (X), other forms are ~X, X’
X
0
1
X
1
0
X
X
X
X
~

## Slide 10
Also known as the conjunction operation;
  output is true (1) only if all inputs are true
Algebraic operators are “·”, “&”, “”
X
0
0
1
1
Y
0
1
0
1
X·Y
0
0
0
1
&
Switching Algebra Operations - AND

## Slide 11
Also known as the disjunction operation;
  output is true (1) if any input is true
Algebraic operators are “+”, “|”, “”
X
0
0
1
1
Y
0
1
0
1
X+Y
0
1
1
1
1
Switching Algebra Operations - OR

## Slide 12: Logic Expressions
  Z = X.Y + X.W operators
  X, Y, W, Z logic literals
  +, . logic variables
  0, 1 logic expression

## Slide 13: Logic Expressions
Terms and Definitions
  Logic Expression - a mathematical formula consisting of logical operators and variables
  Logic Operator - a function that gives a well defined output according to switching algebra
  Logic Variable - a symbol representing the two possible switching algebra values of 0 and 1
  Logic Literal - the values 0 and 1 or a logic variable or it’s complement
  Z = X.Y + X.W logic expression
  X, Y, W, Z logic variables
  +, . operators

## Slide 14
Like standard algebra, switching algebra operators have a precedence of evaluation
  NOT operations have the highest precedence
  AND operations are next
  OR operations are lowest
Parentheses explicitly define the order of operator evaluation
  If in doubt, use PARENTHESES!
Logic Expressions - Precedence

## Slide 16
Each expression can be realized by a logic circuit
Logic Expressions vs. Logic Circuits
F1 = x+y’z

## Slide 17
Logic Expressions vs. Logic Circuits

## Slide 18
Each expression can be realized by a logic circuit
Multiple expressions for a single function
The simpler an expression is, the faster and cheaper its corresponding circuit is
So we try to simplify logic expressions if possible
We call it ‘minimization’
Logic Expressions vs. Logic Circuits

## Slide 19: Logic Expression Minimization
Given a logic expression, the goal is to find another expression that:
  a) has the same truth-table
  b) has fewer variables per term
  c) has fewer terms
  d) needs less logic to implement
  Example: E = A.B.C.D + A.B.C.D’ = A.B.C
There are three main manual methods
  Algebraic minimization
  Karnaugh Map minimization
  Quine-McCluskey (tabular) minimization
    [Assignment: Read this from the web]

## Slide 20: Algebraic Minimization
Process is to apply the switching algebra postulates, laws, and theorems (that will follow) to transform the original expression
  Hard to recognize when a particular law can be applied
  Difficult to know if resulting expression is truly minimal
  Very easy to make a mistake
    Incorrect complementation
    Dropped variables

## Slide 21
Involution:
Switching Algebra - Laws and Theorems

## Slide 22
Identity:
Switching Algebra - Laws and Theorems

## Slide 23
Idempotence:
Switching Algebra - Laws and Theorems

## Slide 24
Associativity:
Switching Algebra - Laws and Theorems

## Slide 25
Adjacency:
Switching Algebra - Laws and Theorems

## Slide 26
Absorption:
Switching Algebra - Laws and Theorems

## Slide 27
Simplification:
Switching Algebra - Laws and Theorems

## Slide 28: How to Prove?
Either use the postulates and simplify
X+(X’.Y) = X+Y (1)
or use distributive postulate
X+YZ = (X+Y).(X+Z)
So (1) can be simplified as:
(X+X’).(X+Y) = 1.(X+Y) = X+Y

## Slide 29
Truth Table Approach (for verification)
X Y X+(X’.Y) X+Y
0 0 0 0
0 1 1 1
1 0 1 1
1 1 1 1
Two output columns are the same!
How to Prove?

## Slide 30
Consensus:
Switching Algebra - Laws and Theorems

## Slide 31
DeMorgan’s Theorem:
General form:
Switching Algebra - Laws and Theorems

## Slide 32
Very useful for complementing function expressions:
DeMorgan's Theorem

## Slide 33: Minimization via Adjacency
Adjacency is easy to use and very powerful
  Look for two terms that are identical except for one variable
  Application removes one term and one variable from the remaining term

## Slide 34
Adjacencies
Duplicate 3rd. term and rearrange (X+X=X)
Apply adjacency on “term pairs”
Example of Adjacency Minimization

## Slide 35: Another Algebraic Simplification Example
W = X’Y’Z+X’Y’Z’+XYZ+X’YZ+X’YZ’
= X’Y’+YZ +X’Z’
There are other solutions, too!