## Slide 1
CENG-232 Logic Design
Week 4
Combinational Logic Design

## Slide 2: Combinational Logic
One or more digital signal inputs
One or more digital signal outputs
Outputs are only functions of current input values (ideal) plus logic propagation delays
Combinational Logic
I1
Im
O1
On

## Slide 3: Combinational Logic (Cont’d.)
Combinational logic has no memory!
  Outputs are only function of current input combination
  Nothing is known about past events
  Repeating a sequence of inputs always gives the same output sequence
Sequential logic (covered later) does have memory
  Repeating a sequence of inputs can result in an entirely different output sequence

## Slide 4: Design Hierarchy
Large systems are usually too complex to design as a single entity
  i.e., a 16 bit binary adder has 32 inputs and therefore there are 2^32 rows in the truth table!
System is usually partitioned into smaller parts which are further partitioned …
This defines a hierarchy of design from complex to simple;
  “top to bottom”

## Slide 5: Design Methodologies
There are two basic approaches to system design:
  Top-down and Bottom-up.
Top-Down: start at the top system level and decompose into ever simpler subsystems and components
Bottom-Up: start with known low-level building blocks and put them together into increasing complex functions
Ideally either can be used to design a combinational system.

## Slide 6: Concurrent Design
The practical approach is to combine the two
  Basic top-down to provide proper decomposition and validation
  BUT as you decompose functions, be aware of:
    already existing and available components
    component to component interface characteristics
    reality - cost, size, weight, power, etc.
If done properly, you end up with a low-cost practical solution that works!

## Slide 7: Rapid Prototyping and CAD
Rapid prototyping assumes we can built many different versions and see which ones work
  Programmable logic is vital to this approach
  Good development tools are also essential
Hardware description languages are the way we quickly specify and change our designs

## Slide 8: Hardware Description Languages (HDLs)
Two main HDLs are being used today
  VHDL
  Verilog
Both are IEEE standards
Both allow us to specify logic designs as textual descriptions
  BE AWARE - both look like a software procedure but are describing HARDWARE!
    Concurrency!!!
We will use Verilog

## Slide 9: Logic Synthesis
After writing the HDL program:
Logic synthesis translates the HDL to our hardware implementation
  1st phase translates HDL to a generic, ideal logic description
    logic expressions are generated and minimized
    allows us to verify functional operation
  2nd phase translates the design to the final physical device
    complexity, speed, delays, power must be addressed
    we can then simulate physical operation of device

## Slide 10: Different Aspects of Digital Logic Implementation
Circuit Properties
  logic representation
  size
  weight
  speed
  power
  package
  temperature
  noise immunity
  cost
Levels of Integration
  SSI, MSI, LSI, VLSI
Circuit Technology
  Digital Logic Families

## Slide 11: Levels of Integration
Small Scale Integration (SSI)
  <10 gates usually
Medium Scale Integration (MSI)
  10 to 1000 gates
  Decoders, adders, multiplexers
  Registers and counters
Large Scale Integration (LSI)
  Thousands of gates
  processors, memory chips, PLDs
Very Large Scale Integration (VLSI)
  Millions of gates in a single package
  Large memory arrays, complex micro computer chips

## Slide 12: Digital Logic Families
TTL : Transistor-transistor logic
  In use for 50 years
  Considered to be the standard
ECL: Emitter-coupled logic
  Has advantage in high-speed operation
MOS: Metal-oxide semiconductor
  Suitable for circuits that need high component density
CMOS: Complementary metal-oxide semiconductor
  Low power consumption
  Handheld computers, cameras, etc.
GaAs: Galium Arsenide
SiGe: Silicon-germanium

## Slide 13: Technology Parameters
Fan-in
Fan-out
Noise margin
Propagation delay
Power dissipation

## Slide 14: Fan-In
For logic gates, it’s the max number of inputs to a specific gate
  Defined by gate design; usually limited to a max of 4 or 5
  E.G. 74LS08 is a Quad, 2-input AND device
    4 AND gates in package, each AND has 2 inputs
When you have more variables than your gate’s inputs
  Cascade gates, transform function, etc.

## Slide 15: Fan-Out
Fan-out is usually defined as the max number of “standard” logic gate inputs that can be connected to a logic gate output
  Specifies the “drive” capability of an output
If an output is overloaded, other characteristics such as noise margin, rise & fall times are degraded
Different logic types are affected by “overload” in different ways

## Slide 16: Noise Margin
Noise Margin defines how much noise can be induced onto a logic signal and still be correctly recognized as a high or low level
  Difference between output high or low level and input level that will recognized as high or low
Voh = 2.8 v
Vih = 2.4 v
Vil = 0.8 v
Vol = 0.4 v
Noise margin high = 0.4 v
Noise margin low = 0.4 v
Transition region; neither Hi or Lo!
TTL
Logic
Levels

## Slide 17: Propagation Delay
Real devices do not have zero delay!
Propagation delays are measured from input change to output change (tPD)
  Usually referenced to 50% point on transition
Gates usually have different delays for the output low to high (tLH) and high to low (tHL)
Best to design using the max of the two
Not all input changes show up at the output
  Gate may not respond to a narrow pulse

## Slide 18: Propagation Delay and Glitches
From http://www.designcabana.com/knowledge/electrical/electronics/digital/propag/

## Slide 19: Power Dissipation
The quantity of electrical power that is dissipated by the device as heat
  Devices have temperature operating range that the device cannot exceed
Power dissipation is mainly static or dynamic depending on the logic type
  TTL/ECL dissipation is mainly static and therefore independent of signal rate of change
  CMOS dissipation is mainly dynamic and increases linearly with changing signals

## Slide 20: Positive and negative logic
We have 1 and 0 in Digital Logic
We have High Voltage and Low Voltage in the Digital Circuit
There are two ways to assign voltage states to logic states

## Slide 21: Positive and negative logic
Hardware manufacturers define their gates using signal values such as H and L.
The TTL chips with part numbers 7408 and 7432 generate outputs according to the function table below.
The same physical gate can operate either as a positive-logic AND gate or as a negative-logic OR gate.

## Slide 22: An example
This notation indicates that the alarm will be enabled when X is low.
From http://sce2.umkc.edu/csee/hieberm/281_new/lectures/basic-electrical-components/pos-neg-logic.html

## Slide 23: Signal Active States and Bubbles
Primarily applies to control signals; used to denote when a condition is active or enabled
  Symbol pins without bubbles denote active-1
  Symbol pins with bubbles denote active-0
  Active State - signal state (0 or 1) that indicates the assertion of some condition or action
    Active-1 (active high) is when active state is logic 1
    Active-0 (active low) is when active state is logic 0

## Slide 24: Active States and Bubbles (Cont’d.)
Inverter (NOT) has two different forms
Input asserted
active-1
Output asserted
active-0
Input asserted
active-0
Output asserted
active-1

## Slide 25: Alternative Symbols
The NOT example can be extended to all logic gates
  Each logic gate has two equivalent symbols
    The one we’ve seen so far for active-1 inputs
    The alternate for active-0 inputs
  In each case the gate operates the same
    The only difference is how we interpret the values

## Slide 26: AND Gate Alternate Symbol
X
0
0
1
1
Y
0
1
0
1
X·Y
0
0
0
1
X
F
F
T
T
Y
F
T
F
T
X·Y
F
F
F
T
X
T
T
F
F
Y
T
F
T
F
X+Y
T
T
T
F
Active-1
Active-0

## Slide 27: OR Gate Alternate Symbol
X
0
0
1
1
Y
0
1
0
1
X+Y
0
1
1
1
X
F
F
T
T
Y
F
T
F
T
X+Y
F
T
T
T
X
T
T
F
F
Y
T
F
T
F
X·Y
T
F
F
F
Active-1
Active-0

## Slide 28: Other Gate Alternative Symbols
NAND
NOR
XOR
XNOR
Active-1 Active-0

## Slide 29: Signal Naming Conventions
The problem is how to distinguish between active-1 and active-0 signals.
  Barring a signal name to designate active-0 is not recommended
    Is A active-0 or NOT A??
  Use suffix of ‘_0’; (i.e. A_0) after signal name
  Use suffix of ‘_LO’ or ‘_L’
  Use suffix of ‘_BAR’
No matter what you use, BE CONSISTENT!

## Slide 30: Signal Naming Conventions
To denote an active-0 signal, we use one of the following naming conventions:
  Suffix of ‘_0’; (i.e. A_0) after signal name
  Suffix of ‘_LO’ or ‘_L’
  Suffix of ‘_BAR’

## Slide 31: Signal Naming (Cont’d.)
Active-0 signal naming and symbol bubbles require some thought to interpret properly
A_L
(active-0)
A
(active-1)
A_L
(active-0)
A
(active-1)

## Slide 32: Naming and Alternate Symbols
Proper active-0 signal naming and usage of alternate symbols can clarify the circuit intent
HEAT
TEMP1_L
TEMP2_L
This is really a NOR gate
TEMP1_L
TEMP2_L
HEAT
TEMP1
TEMP2

## Slide 33: Naming and Alternate Symbols
Proper active-0 signal naming and usage of alternate symbols can clarify the circuit intent
HEAT
TEMP1_L
TEMP2_L

## Slide 34: Previously on CENG 232
Digital vs Analog
Binary Digital Systems
  Represented physically by voltage, or ..
Boolean Algebra (Switching Algebra)
  A way to express logic functions algebraically
Simplify Boolean functions
  Algebraically, or using K-maps
  To have economical implementations
Digital Gates that manipulates the signals to achieve functionality
Analyze the behavior of a logic circuit
  Literal
  Symbolic

## Slide 35: Combinational Circuit Design

## Slide 36: Design Methodology
We start with some form of a problem statement
  Usually just text; ambiguous, poorly stated
We must produce a design representation
  Minimized switching algebra expressions
The primary problem we have, is first to concisely define the true problem we are to solve
  Define the “system” requirements

## Slide 37: Design Methodology (Cont’d.)
Step 1 - Break down the problem statement
  Identify system inputs and outputs
  Extract the stated input-output relationship(s)
  State the above as system (black-box) level requirements. BE PRECISE!
Step 2 - Perform initial system definition
  Define interface variables and representation
    If representation is not defined in problem statement, make preliminary assignment
  Restate I/O relationship as algorithm, equation, simulation, etc.

## Slide 38: Design Methodology (Cont’d.)
Step 3 - Translate relationships to logic representation
  Construct truth table, generate S.A. expressions
  This is the formal statement of the I/O relationship(s)
Step 4 - Generate minimal set of logic expressions
  Rapid prototyping development tools
  Karnaugh maps, Quine-McCluskey, etc.

## Slide 39: Design Methodology (Cont’d.)
Step 5 - Implement and verify the design
  Rapid prototyping (programmable logic) - target device and simulate timing behavior
  Otherwise, draw schematic
    Lots of ways to actually implement the equations
    Must know what logic family you are to use.
  Acid test is to build the circuit and test it
    Must operate in real-world environment
    Noise, temperature, other factors may cause problems

## Slide 40: BCD to XS3 Example
Initial Statement: “Design a circuit to convert BCD to XS3.”
  1) We need to restate and translate this to specific requirements
    R1: The circuit shall input one BCD digit
    R2: The circuit shall output one XS3 digit
    R3: The XS3 output shall be the equivalent decimal value as the BCD input value
BCD(X) to XS3(X)
BCD
digit
XS3
digit

## Slide 41
BCD to XS3 Example

## Slide 42: BCD to XS3 Example (Cont’d.)
2) Now we need to define the interfaces in detail
    We know that the input is one decimal digit in BCD representation, i.e. 4 bits, BCD := {b3, b2, b1, b0}
    The output is one XS3 decimal digit, which is also 4 bits, i.e. XS3 := {x3, x2, x1, x0}
    Usually, well known representations don’t need explicit definition; when in doubt, DEFINE IT!
3) Now we use a truth table to define the logical input/output relationship
    Only 10 of 16 possible input combinations are valid
    We’ll assume last 6 won’t occur; i.e. are don’t cares

## Slide 43: BCD to XS3 Example (Cont’d.)
b0
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
b1
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
b2
0
0
0
0
1
1
1
1
0
0
0
0
1
1
1
1
b3
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
x0
1
0
1
0
1
0
1
0
1
0
-
-
-
-
-
-
x1
1
0
0
1
1
0
0
1
1
0
-
-
-
-
-
-
x2
0
1
1
1
1
0
0
0
0
1
-
-
-
-
-
-
x3
0
0
0
0
0
1
1
1
1
1
-
-
-
-
-
-
Note: Don’t cares
can work to our
advantage during
minimization; we
can assign either
0 or 1 as needed.

## Slide 44: BCD to XS3 Example (Cont’d.)
4) Now we can generate the logical expressions for the outputs (canonical SofP form)

## Slide 45: BCD to XS3 Example (Cont’d.)
The minimized equations are as follows:

## Slide 46: BCD to XS3 Example (Cont’d.)
b0
b1
b2
b3
x3
x2
x1
x0

## Slide 47: Technology Mapping
Translation of the “ideal” circuit design to actual hardware must account for the implementation method
  ASICs (Application specific integrated circuit): full custom, standard cell, or gate arrays
  Programmable logic: FPGAs or PLDs
  Gate types, input configurations available
Vendors supply you with a set of logic gate design patterns known as a cell library
  Defines implementation rules as well as gate types
CAD tools then use the provided library to map the ideal design to the physical implementation
  Translates design to preferred logic types
  Checks for problems; fan-out, propagation times exceeded

## Slide 48: Verification
Design verification is much more difficult with VLSI ASICs than with SSI designs
  Lots more signals and less accessibility
VLSI: Very-large-scale integration is the process of creating an integrated circuit by combining thousands of transistors into a single chip.
ASIC: Application specific integrated circuit
SSI: Small-scale integration. The early integrated circuits were SSI.

## Slide 49: Verification
Ensuring that the final device actually works is mandatory and can also be hard to do
  Must start with good requirements (validation)
    It’s really bad to find out your design meets the stated requirements but it’s not what the customer wanted
  Done at different stages of the development
    Simulation used during the design capture and implementation mapping phase
    Functional and parametric testing after device fabrication