## Slide 1: Register Transfer and Microoperations
Acknowledgment: Most of the slides are adapted from Prof. Hyunsoo Yoon’s slides.

## Slide 2: Register transfer level (RTL)
The modules of a digital system can be best defined by
  A set of registers, and
  The operations that are performed on data stored in them.
  Example operations: shift, count, load and clear.
A digital system is represented at the RTL when it is specified by the following 3 components
  (1) The set of registers in the system
  (2) The operations that are performed on the registers
  (3) The control that supervises the sequence of operations in the system.
Starting from this week, RTL specification of a basic computer.

## Slide 3
So far, we have designed digital systems that serve a specific purpose.
But a “computer” is a general purpose device. It is programmable.
A sample program that our basic computer will be able to run:

## Slide 4: BASIC COMPUTER REGISTERS
List of BC Registers
  DR 16 Data Register Holds memory operand
  AR 12 Address Register Holds address for memory
  AC 16 Accumulator Processor register
  IR 16 Instruction Register Holds instruction code
  PC 12 Program Counter Holds address of instruction
  TR 16 Temporary Register Holds temporary data
  INPR 8 Input Register Holds input character
  OUTR 8 Output Register Holds output character
Registers
Registers in the Basic Computer
11
0
PC
15
0
IR
15
0
TR
7
0
OUTR
15
0
DR
15
0
AC
11
0
AR
INPR
0
7
Memory
4096 x 16
CPU

## Slide 5: BASIC COMPUTER REGISTERS
List of BC Registers
  DR 16 Data Register Holds memory operand
  AR 12 Address Register Holds address for memory
  AC 16 Accumulator Processor register
  IR 16 Instruction Register Holds instruction code
  PC 12 Program Counter Holds address of instruction
  TR 16 Temporary Register Holds temporary data
  INPR 8 Input Register Holds input character
  OUTR 8 Output Register Holds output character
Registers
Registers in the Basic Computer
11
0
PC
15
0
IR
15
0
TR
7
0
OUTR
15
0
DR
15
0
AC
11
0
AR
INPR
0
7
Memory
4096 x 16
CPU
Question: how will the data be transferred among these registers, memory and arithmetic-logic unit (ALU) (not shown here)?

## Slide 6: COMMON BUS SYSTEM
Registers
S2
S1
S0
Bus
Memory unit
4096 x 16
LD INR CLR
Address
Read
Write
AR
LD INR CLR
PC
LD INR CLR
DR
LD INR CLR
AC
ALU
E
INPR
IR
LD
LD INR CLR
TR
OUTR
LD
Clock
16-bit common bus
7
1
2
3
4
5
6
  DR 16 Data Register
  AR 12 Address Register
  AC 16 Accumulator
  IR 16 Instruction Register
  PC 12 Program Counter
  TR 16 Temporary Register
  INPR 8 Input Register
  OUTR 8 Output Register

## Slide 7: REGISTER TRANSFER AND MICROOPERATIONS
• Register Transfer Language
• Register Transfer
• Bus and Memory Transfers
• Arithmetic Microoperations
• Logic Microoperations
• Shift Microoperations
• Arithmetic Logic Shift Unit

## Slide 8: SIMPLE DIGITAL SYSTEMS
Combinational and sequential circuits can be used to create simple digital systems.
These are the low-level building blocks of a digital computer.
Simple digital systems are frequently characterized in terms of
  the registers they contain, and
  the operations that they perform.

## Slide 9: MICROOPERATIONS (1)
The operations on the data in registers are called “microoperations”.
The functions built into registers are examples of microoperations
  Shift
  Load
  Clear
  Increment
  …

## Slide 10: MICROOPERATIONS (2)
R  f (R, R)
f: shift, load, clear, increment, add, subtract, complement,
and, or, xor, …
Microoperation: An elementary operation that is performed (during one clock cycle), on the information stored in one or more registers
ALU
(f)
Registers
(R)
1 clock cycle

## Slide 11: Register Transfer Level (RTL)
- Set of registers and their functions
- Microoperations set
    Set of allowable microoperations provided by the organization of the computer
- Control signals that initiate the sequence of
microoperations (to perform the functions)
Definition of the (internal) organization of a computer
Viewing a computer, or any digital system, in this way is called the register transfer level
This is because we’re focusing on
  The system’s registers
  The data transformations in them, and
  The data transfers between them.

## Slide 12: REGISTER TRANSFER LANGUAGE
Rather than specifying a digital system in words, a specific notation is used, register transfer language
For any function of the computer, the register transfer language can be used to describe the (sequence of) microoperations
Register transfer language
  A symbolic language
  A convenient tool for describing the internal organization of digital computers
  Can also be used to facilitate the design process of digital systems.

## Slide 13: DESIGNATION OF REGISTERS
Registers are designated by capital letters, sometimes followed by numbers (e.g., A, R13, IR)
Often the names indicate function:
  MAR - memory address register
  PC - program counter
  IR - instruction register
Registers and their contents can be viewed and represented in various ways
  A register can be viewed as a single entity:
  Registers may also be represented showing the bits of data they contain
MAR

## Slide 14: DESIGNATION OF REGISTERS
R1
Register
Numbering of bits
Showing individual bits
Subfields
PC(H)
PC(L)
15
8
7
0
Common ways of drawing the block diagram of a register
7 6 5 4 3 2 1 0
R2
15
0
Designation of a register
- a register
- portion of a register
- a bit of a register

## Slide 15: REGISTER TRANSFER
Copying the contents of one register to another is a register transfer
A register transfer is indicated as
  R2  R1
  In this case, the contents of register R1 are copied (loaded) into register R2
  A simultaneous transfer of all bits from the source R1 to the destination register R2, during one clock pulse
  Note that this is non-destructive; i.e. the contents of R1 are not altered by copying (loading) them to R2

## Slide 16: REGISTER TRANSFER
A register transfer such as
  R3  R5
  Implies that the digital system has
  the data lines from the source register (R5) to the destination register (R3)
  Parallel load in the destination register (R3)
  Control lines to perform the action

## Slide 17: CONTROL FUNCTIONS
Often actions need to only occur if a certain condition is true
This is similar to an “if” statement in a programming language
In digital systems, this is often done via a control signal, called a control function
  If the signal is 1, the action takes place
This is represented as:
  P: R2  R1
  Which means “if P = 1, then load the contents of register R1 into register R2”, i.e., if (P = 1) then (R2  R1)

## Slide 18: HARDWARE IMPLEMENTATION OF CONTROLLED TRANSFERS
Implementation of controlled transfer
P: R2 R1
Block diagram
Timing diagram
Transfer occurs here
Clock
Load
t
t+1
Clock
R2
R1
Control
Circuit
Load
P
n
The same clock controls the circuits that generate the control function and the destination register
Registers are assumed to use positive-edge-triggered flip-flops

## Slide 19: SIMULTANEOUS OPERATIONS
If two or more operations are to occur simultaneously, they are separated with commas
  P: R3  R5, MAR  IR
Here, if the control function P = 1,
  load the contents of R5 into R3, and
  at the same time (clock), load the contents of register IR into register MAR

## Slide 20: BASIC SYMBOLS FOR REGISTER TRANSFERS
Capital letters Denotes a register MAR, R2
& numerals
Parentheses () Denotes a part of a register R2(0-7), R2(L)
Arrow  Denotes transfer of information R2 R1
Colon : Denotes termination of control function P:
Comma , Separates two micro-operations A B, B A
Symbols
Description Examples

## Slide 21: CONNECTING REGISTERS
In a digital system with many registers, it is impractical to have data and control lines to directly allow each register to be loaded with the contents of every possible other registers
To completely connect n registers, we need ? Lines
  n(n-1) lines
This is O(?)
  O(n2)
  This is not a realistic approach to use in a large digital system
Instead, have one centralized set of circuits for data transfer – THE BUS
Have control circuits to select which register is the source, and which is the destination

## Slide 22: BUS AND BUS TRANSFER
Bus is a path (of a group of wires) over which information is transferred, from any of several sources to any of several destinations.
From a register to bus: BUS  R
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Register A
Register B
Register C
Register D
B
C
D
1
1
1
4 x1
MUX
B
C
D
2
2
2
4 x1
MUX
B
C
D
3
3
3
4 x1
MUX
B
C
D
4
4
4
4 x1
MUX
4-line bus
x
y
select
0
0
0
0
Register A
Register B
Register C
Register D
Bus lines
How can we do it?

## Slide 23: TRANSFER FROM BUS TO A DESTINATION REGISTER
Reg. R0
Reg. R1
Reg. R2
Reg. R3
Bus lines
2 x 4
Decoder
Load
D
0
D
1
D
2
D
3
z
w
Select
E (enable)
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Register A
Register B
Register C
Register D
B
C
D
1
1
1
4 x1
MUX
B
C
D
2
2
2
4 x1
MUX
B
C
D
3
3
3
4 x1
MUX
B
C
D
4
4
4
4 x1
MUX
4-line bus
x
y
select
0
0
0
0
How can we do transfer to the registers?

## Slide 24: TRANSFER FROM BUS TO A DESTINATION REGISTER (USING THREE-STATE BUFFERS)
Three-State Bus Buffers
Bus line with three-state buffers
Y=A if C=1
Y=High-impedance, i.e. disconnected, if C=0
Output Y
Control input C
Select
Enable
0
1
2
3
S0
S1
A0
B0
C0
D0
Bus line for bit 0

## Slide 25: BUS TRANSFER IN RTL
Depending on whether the bus is to be mentioned explicitly or not, register transfer can be indicated as either
or
In the former case, the bus is implicit, but in the latter, it is explicitly indicated
R2 R1
BUS R1, R2  BUS

## Slide 26: MEMORY (RAM)
Memory (RAM) can be thought as a sequential circuit containing some number of registers
These registers hold the words of memory
Each of the r registers is indicated by an address
These addresses range from 0 to r-1
Each register can hold n bits of data (a word)
Assume the RAM contains r = 2k words. It needs the following
  n data input lines
  n data output lines
  k address lines
  A Read control line
  A Write control line
data input lines
data output lines
n
n
k
address lines
Read
Write
RAM
unit

## Slide 27: MEMORY TRANSFER
Collectively, the memory is viewed at the register level as a device, M.
Since it contains multiple locations, we must specify which address in memory we will be using
This is done by indexing memory references
Memory is usually accessed in computer systems by putting the desired address in a special register, the Memory Address Register (MAR, or AR)
When memory is accessed, the contents of the MAR get sent to the memory unit’s address lines
MAR
Memory
unit
Read
Write
Data in
Data out
M

## Slide 28: MEMORY READ
To read a value from a location in memory and load it into a register, the register transfer language notation looks like this:
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Read (= 1) gets sent to the memory unit
  The contents of the specified address are put on the memory’s output data lines
  These get sent over the bus to be loaded into register R1
R1  M[MAR]

## Slide 29: MEMORY WRITE
To write a value from a register to a location in memory looks like this in register transfer language:
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Write (= 1) gets sent to the memory unit
  The values in register R1 get sent over the bus to the data input lines of the memory
  The values get loaded into the specified address in the memory
M[MAR]  R1

## Slide 30: SUMMARY OF R. TRANSFER MICROOPERATIONS
A B Transfer content of reg. B into reg. A
AR DR(AD) Transfer content of AD portion of reg. DR into reg. AR
A  constant Transfer a binary constant into reg. A
ABUS R1, R2 ABUS Transfer content of R1 into bus A and, at the same time,
transfer content of bus A into R2
AR Address register (a.k.a. MAR)
DR Data register
M[R] Memory word specified by reg. R
M Equivalent to M[AR]
DR  M Memory read operation: transfers content of
memory word specified by AR into DR
M  DR Memory write operation: transfers content of
DR into memory word specified by AR

## Slide 31: MICROOPERATIONS
Computer system microoperations are of four types:
- Register transfer microoperations
- Arithmetic microoperations
- Logic microoperations
- Shift microoperations

## Slide 32: ARITHMETIC MICROOPERATIONS
Summary of Typical Arithmetic Micro-Operations
  R3  R1 + R2 Contents of R1 plus R2 transferred to R3
  R3  R1 - R2 Contents of R1 minus R2 transferred to R3
  R2  R2’ Complement the contents of R2
  R2  R2’+ 1 2's complement the contents of R2 (negate)
  R3  R1 + R2’+ 1 subtraction
  R1  R1 + 1 Increment
  R1  R1 - 1 Decrement
The basic arithmetic microoperations are
  Addition
  Subtraction
  Increment
  Decrement
The additional arithmetic microoperations are
  Add with carry
  Subtract with borrow
  Negation,
  Transfer/Load
  etc. …

## Slide 33: BINARY ADDER / SUBTRACTOR / INCREMENTER
Binary Adder-Subtractor
Binary Incrementer
Binary Adder
Arithmetic Microoperations
Notes: When M=1, binary adder-suibtractor implements A+B’+1, that is A-B. Why?
Consider Z=A XOR B. When B is 1, Z is A’ (check). So, when M=1, B is inverted and C0 is 1.

## Slide 34: ARITHMETIC CIRCUIT
S1
S0
0
1
2
3
4x1
MUX
X0
Y0
C0
C1
D0
FA
S1
S0
0
1
2
3
4x1
MUX
X1
Y1
C1
C2
D1
FA
S1
S0
0
1
2
3
4x1
MUX
X2
Y2
C2
C3
D2
FA
S1
S0
0
1
2
3
4x1
MUX
X3
Y3
C3
C4
D3
FA
Cout
A0
B0
A1
B1
A2
B2
A3
B3
0
1
S0
S1
Cin
S1 S0 Cin Y Output Microoperation
0 0 0 B D = A + B Add
0 0 1 B D = A + B + 1 Add with carry
0 1 0 B’ D = A + B’ Subtract with borrow
0 1 1 B’ D = A + B’+ 1 Subtract
1 0 0 0 D = A Transfer A
1 0 1 0 D = A + 1 Increment A
1 1 0 1 D = A - 1 Decrement A
1 1 1 1 D = A Transfer A

## Slide 35: LOGIC MICROOPERATIONS
Specify binary operations on the strings of bits in registers
  Logic microoperations are bit-wise operations, i.e., they work on the individual bits of data
  useful for bit manipulations on binary data
  useful for making logical decisions based on the bit value
There are, in principle, 16 different logic functions that can be defined over two binary input variables
However, most systems only implement four of these
  AND (), OR (), XOR (), Complement/NOT
The others can be created from combination of these
0 0 0 0 0 … 1 1 1
0 1 0 0 0 … 1 1 1
1 0 0 0 1 … 0 1 1
1 1 0 1 0 … 1 0 1
A B F0 F1 F2 … F13 F14 F15
Why?

## Slide 36: LIST OF LOGIC MICROOPERATIONS
List of Logic Microoperations
- 16 different logic operations with 2 binary vars.
- n binary vars → functions
2
2
n
Truth tables for 16 functions of 2 variables (1-bit each) and the
corresponding 16 logic micro-operations
Boolean
Function
Micro-
Operations
Name
x 0 0 1 1
y 0 1 0 1
  0 0 0 0 F0 = 0 F  0 Clear
  0 0 0 1 F1 = xy F  A  B AND
  0 0 1 0 F2 = xy' F  A  B’
  0 0 1 1 F3 = x F  A Transfer A
  0 1 0 0 F4 = x'y F  A’ B
  0 1 0 1 F5 = y F  B Transfer B
  0 1 1 0 F6 = x  y F  A  B Exclusive-OR
  0 1 1 1 F7 = x + y F  A  B OR
  1 0 0 0 F8 = (x + y)' F  A  B)’ NOR
  1 0 0 1 F9 = (x  y)' F  (A  B)’ Exclusive-NOR
  1 0 1 0 F10 = y' F  B’ Complement B
  1 0 1 1 F11 = x + y' F  A  B
  1 1 0 0 F12 = x' F  A’ Complement A
  1 1 0 1 F13 = x' + y F  A’ B
  1 1 1 0 F14 = (xy)' F  (A  B)’ NAND
  1 1 1 1 F15 = 1 F  all 1's Set all to 1's

## Slide 37: HARDWARE IMPLEMENTATION OF LOGIC MICROOPERATIONS
0 0 F = A  B AND
0 1 F = AB OR
1 0 F = A  B XOR
1 1 F = A’ Complement
S1 S0
Output
-operation
Function table
B
A
S
S
F
1
0
i
i
i
0
1
2
3
4 X 1
MUX
Select

## Slide 38: APPLICATIONS OF LOGIC MICROOPERATIONS
Logic microoperations can be used to manipulate individual bits or a portions of a word in a register
Consider the data in a register A. In another register, B, is bit data that will be used to modify the contents of A
  Selective-set A  A + B
  Selective-complement A  A  B
  Selective-clear A  A • B’
  Mask (Delete) A  A • B
  Clear A  A  B
  Insert A  (A • B) + C
  Compare A  A  B
  . . .

## Slide 39: SELECTIVE SET
In a selective set operation, the bit pattern in B is used to set certain bits in A
1 1 0 0 At
1 0 1 0 B
1 1 1 0 At+1 (A  A + B)
If a bit in B is set to 1, that same position in A gets set to 1, otherwise that bit in A keeps its previous value

## Slide 40: SELECTIVE COMPLEMENT
In a selective complement operation, the bit pattern in B is used to complement certain bits in A
1 1 0 0 At
1 0 1 0 B
0 1 1 0 At+1 (A  A  B)
If a bit in B is set to 1, that same position in A gets complemented from its original value, otherwise it is unchanged

## Slide 41: SELECTIVE CLEAR
In a selective clear operation, the bit pattern in B is used to clear certain bits in A
1 1 0 0 At
1 0 1 0 B
0 1 0 0 At+1 (A  A  B’)
If a bit in B is set to 1, that same position in A gets set to 0, otherwise it is unchanged

## Slide 42: MASK OPERATION
In a mask operation, the bit pattern in B is used to clear certain bits in A
1 1 0 0 At
1 0 1 0 B
1 0 0 0 At+1 (A  A  B)
If a bit in B is set to 0, that same position in A gets set to 0, otherwise it is unchanged

## Slide 43: COMPLEMENT OPERATION
In a clear operation, if the bits in the same position in A and B are the same, they are cleared in A, otherwise they are set in A
1 1 0 0 At
1 0 1 0 B
0 1 1 0 At+1 (A  A  B)

## Slide 44: INSERT OPERATION
An insert operation is used to introduce a specific bit pattern into A register, leaving the other bit positions unchanged
This is done as
  A mask operation to clear the desired bit positions, followed by
  An OR operation to introduce the new bits into the desired positions

## Slide 45: INSERT OPERATION
Example
  Suppose you wanted to introduce 1010 into the low order four bits of A:
      1101 1000 1011 0001 A (Original)
      1101 1000 1011 1010 A (Desired)
1101 1000 1011 0001 A (Original)
1111 1111 1111 0000 Mask (AND op.)
1101 1000 1011 0000 A (Intermediate)
0000 0000 0000 1010 Added bits (OR op.)
1101 1000 1011 1010 A (Desired)
End of logic microoperations

## Slide 46: SHIFT MICROOPERATIONS
There are three types of shifts
  Logical shift
  Circular shift
  Arithmetic shift
What differentiates them is the information that goes into the serial input
Serial
input
A right shift operation
A left shift operation
Serial
input

## Slide 47: LOGICAL SHIFT
In a logical shift the serial input to the shift is a 0.
A right logical shift operation:
A left logical shift operation:
In a Register Transfer Language, the following notation is used
  shl for a logical shift left
  shr for a logical shift right
  Examples:
    R2  shr R2
    R3  shl R3
0
0

## Slide 48: CIRCULAR SHIFT
In a circular shift the serial input is the bit that is shifted out of the other end of the register.
A right circular shift operation:
A left circular shift operation:
In a RTL, the following notation is used
  cil for a circular shift left
  cir for a circular shift right
  Examples:
    R2  cir R2
    R3  cil R3

## Slide 49: ARITHMETIC SHIFT
An arithmetic shift is meant for signed binary numbers (integers)
  An arithmetic left shift multiplies a signed number by two
  An arithmetic right shift divides a signed number by two
The main distinction of an arithmetic shift is that it must keep the sign of the number the same as it performs the multiplication or division
A right arithmetic shift operation:
A left arithmetic shift operation:
sign
bit
0
sign
bit
Example: Using a 5-bit two’s complement system, left-shift 00011, 11011 and 10110.

## Slide 50: ARITHMETIC SHIFT
A left arithmetic shift operation must be checked for the overflow
0
V
Before the shift, if the leftmost two
bits differ, the shift will result in an
overflow
In a RTL, the following notation is used
  ashl for an arithmetic shift left
  ashr for an arithmetic shift right
  Examples:
    R2  ashr R2
    R3  ashl R3
sign
bit

## Slide 51: HARDWARE IMPLEMENTATION OF SHIFT MICROOPERATIONS
S
0
1
H0
MUX
S
0
1
H1
MUX
S
0
1
H2
MUX
S
0
1
H3
MUX
Select
0 for shift right (down)
1 for shift left (up)
Serial
input (IR)
A0
A1
A2
A3
Serial
input (IL)
Only T-junctions are connections here!
Notes: In a processor unit with many registers it is more efficient to implement the shift operation with a combinational circuit.
In this way the content of a register that has to be shifted is first placed onto a common bus whose output is connected to the combinational shifter, and the shifted number is then loaded back into the register.
This requires only one clock pulse for loading the shifted value into the register.

## Slide 52: ARITHMETIC LOGIC SHIFT UNIT
  S3 S2 S1 S0 Cin Operation Function
  0 0 0 0 0 F = A Transfer A
  0 0 0 0 1 F = A + 1 Increment A
  0 0 0 1 0 F = A + B Addition
  0 0 0 1 1 F = A + B + 1 Add with carry
  0 0 1 0 0 F = A + B’ Subtract with borrow
  0 0 1 0 1 F = A + B’+ 1 Subtraction
  0 0 1 1 0 F = A - 1 Decrement A
  0 0 1 1 1 F = A TransferA
  0 1 0 0 X F = A  B AND
  0 1 0 1 X F = A B OR
  0 1 1 0 X F = A  B XOR
  0 1 1 1 X F = A’ Complement A
  1 0 X X X F = shr A Shift right A into F
  1 1 X X X F = shl A Shift left A into F
Arithmetic
Circuit
Logic
Circuit
C
C
4 x 1
MUX
Select
0
1
2
3
F
S3
S2
S1
S0
B
A
i
A
D
A
E
shr
shl
i+1
i
i
i
i+1
i-1
i
i
Notes: Instead of having individual registers performing the microoperations directly, computer systems employ a number of storage registers connected to a common operational unit called an arithmetic logic unit, abbreviated ALU