## Slide 1: Basic Computer Organization Designing your first computer
Acknowledgment: Most of the slides are adapted from Prof. Hyunsoo Yoon’s slides.

## Slide 2
A sample program that our basic computer will be able to run:

## Slide 3: BASIC COMPUTER (BC) ORGANIZATION AND DESIGN
• Instruction Codes
• Computer Registers
• Computer Instructions
• Timing and Control
• Instruction Cycle
• Memory Reference Instructions
• Input-Output and Interrupts
• Complete Computer Description
• Design of Basic Computer
• Design of Accumulator Logic

## Slide 4: INTRODUCTION
Every processor type has its own design (different registers, buses, microoperations, machine instructions, etc)
A modern processor is a very complex device
It contains
  Many registers
  Multiple arithmetic units, for both integer and floating point calculations
  The ability to pipeline several consecutive instructions to speed execution
  Etc.
However, to understand how processors work, we will start with a simplified processor model. We’ll call this the “Basic Computer.”
This is similar to what real processors were like ~30 years ago
We will use this to introduce processor organization and the relationship of the RTL model to the higher level computer processor

## Slide 5: BASIC COMPUTER (BC) REGISTERS
List of BC Registers
  DR 16 Data Register Holds memory operand
  AR 12 Address Register Holds address for memory
  AC 16 Accumulator Processor register
  IR 16 Instruction Register Holds instruction code
  PC 12 Program Counter Holds address of instruction
  TR 16 Temporary Register Holds temporary data
  INPR 8 Input Register Holds input character
  OUTR 8 Output Register Holds output character
Registers in the Basic Computer
11
0
PC
15
0
IR
15
0
TR
7
0
OUTR
15
0
DR
15
0
AC
11
0
AR
INPR
0
7
Memory
4096 x 16
CPU

## Slide 6: THE BASIC COMPUTER
The Basic Computer has two components, a processor and memory
The memory has 4096 words in it
  4096 = 212, so it takes 12 bits to select a word in memory
Each word is 16 bits long
CPU
RAM
0
4095
0
15

## Slide 7: INSTRUCTIONS
Instruction codes
Program
  A sequence of (machine) instructions
(Machine) Instruction
  A group of bits that tell the computer to perform a specific operation (a sequence of micro-operations)
The instructions of a program, along with any needed data are stored in memory
The CPU reads the next instruction from memory
It is placed in an Instruction Register (IR)
Control unit then translates the instruction into the sequence of microoperations necessary to implement it

## Slide 8: INSTRUCTION FORMAT
Instruction codes
A computer instruction is often divided into two parts
  An opcode (Operation Code) that specifies the operation for that instruction
  An address that specifies the registers and/or locations in memory to use for that operation
In the Basic Computer, since the memory contains 4096 (= 212) words, we needs 12 bit to specify which memory address this instruction will use
In the Basic Computer, bit 15 of the instruction specifies the addressing mode (0: direct addressing, 1: indirect addressing)
Since the memory words, and hence the instructions, are 16 bits long, that leaves 3 bits for the instruction’s opcode
Opcode
Address
Instruction Format
15
14
12
0
I
11
Addressing
mode

## Slide 9: ADDRESSING MODES
Instruction codes
The address field of an instruction can represent either
  Direct address: the address in memory of the data to use (the address of the operand), or
  Indirect address: the address in memory of the address in memory of the data to use
Effective Address (EA)
  The address, that can be directly used without modification to access an operand for a computation-type instruction, or as the target address for a branch-type instruction
0
ADD
457
22
Operand
457
1
ADD
300
35
1350
300
Operand
1350
+
AC
+
AC
Direct addressing
Indirect addressing

## Slide 10: PROCESSOR REGISTERS
Instruction codes
A processor has many registers to hold instructions, addresses, data, etc
The processor has a register, the Program Counter (PC) that holds the memory address of the next instruction to get
  Since the memory in the Basic Computer only has 4096 locations, the PC only needs 12 bits
In a direct or indirect addressing, the processor needs to keep track of what locations in memory it is addressing: The Address Register (AR) is used for this
  The AR is a 12 bit register in the Basic Computer
When an operand is found, using either direct or indirect addressing, it is placed in the Data Register (DR). The processor then uses this value as data for its operation
The Basic Computer has a single general purpose register – the Accumulator (AC)

## Slide 11: PROCESSOR REGISTERS
Instruction codes
The significance of a general purpose register is that it can be referred to in instructions
  e.g. load AC with the contents of a specific memory location; store the contents of AC into a specified memory location
Often a processor will need a scratch register to store intermediate results or other temporary data; in the Basic Computer this is the Temporary Register (TR)

## Slide 12: PROCESSOR REGISTERS
Instruction codes
The Basic Computer uses a very simple model of input/output (I/O) operations
  Input devices are considered to send 8 bits of character data to the processor
  The processor can send 8 bits of character data to output devices
The Input Register (INPR) holds an 8 bit character gotten from an input device
The Output Register (OUTR) holds an 8 bit character to be send to an output device

## Slide 13: BASIC COMPUTER REGISTERS
List of BC Registers
  DR 16 Data Register Holds memory operand
  AR 12 Address Register Holds address for memory
  AC 16 Accumulator Processor register
  IR 16 Instruction Register Holds instruction code
  PC 12 Program Counter Holds address of instruction
  TR 16 Temporary Register Holds temporary data
  INPR 8 Input Register Holds input character
  OUTR 8 Output Register Holds output character
Registers
Registers in the Basic Computer
11
0
PC
15
0
IR
15
0
TR
7
0
OUTR
15
0
DR
15
0
AC
11
0
AR
INPR
0
7
Memory
4096 x 16
CPU

## Slide 14: COMMON BUS SYSTEM
Registers
The registers in the Basic Computer are connected using a bus
This gives a savings in circuitry over complete connections between registers

## Slide 15: COMMON BUS SYSTEM
Registers
S2
S1
S0
Bus
Memory unit
4096 x 16
LD INR CLR
Address
Read
Write
AR
LD INR CLR
PC
LD INR CLR
DR
LD INR CLR
AC
ALU
E
INPR
IR
LD
LD INR CLR
TR
OUTR
LD
Clock
16-bit common bus
7
1
2
3
4
5
6

## Slide 16: COMMON BUS SYSTEM
Registers
AR
PC
DR
L
I
C
L
I
C
L
I
C
AC
L
I
C
ALU
E
IR
L
TR
L
I
C
OUTR
LD
INPR
Memory
4096 x 16
Address
Read
Write
16-bit Common Bus
7
1
2
3
4
5
6
S0
S1
S2

## Slide 17: COMMUNICATION OVER THE BUS
Reg. R0
Reg. R1
Reg. R2
Reg. R3
Bus lines
2 x 4
Decoder
Load
D
0
D
1
D
2
D
3
z
w
Select
E (enable)
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Register A
Register B
Register C
Register D
B
C
D
1
1
1
4 x1
MUX
B
C
D
2
2
2
4 x1
MUX
B
C
D
3
3
3
4 x1
MUX
B
C
D
4
4
4
4 x1
MUX
4-line bus
x
y
select
0
0
0
0
This is from our previous lecture:
MUX select lines choose which register is input to the bus.
Decoder(s) in the control unit decide which register accepts input from the bus (by setting the Load input).

## Slide 18: COMMON BUS SYSTEM
Registers
Three control lines, S2, S1, and S0 control which register the bus selects as its input
Either one of the registers will have its load signal activated, or the memory will have its read write signal activated
  Will determine where the data from the bus gets loaded
The 12-bit registers, AR and PC, have 0’s loaded onto the bus in the high order 4 bit positions
When the 8-bit register OUTR is loaded from the bus, the data comes from the low order 8 bits on the bus
0 0 0 x
0 0 1 AR
0 1 0 PC
0 1 1 DR
1 0 0 AC
1 0 1 IR
1 1 0 TR
1 1 1 Memory
S2 S1 S0 Register

## Slide 19: BASIC COMPUTER INSTRUCTIONS
Instructions
There are three type of instructions in our basic computer:
15 14
12 11
0
I
Opcode
Address
Memory-Reference Instructions (OP-code = 000 ~ 110)
Register-Reference Instructions (OP-code = 111, I = 0)
Input-Output Instructions (OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 20: BASIC COMPUTER INSTRUCTIONS
Hex Code
Symbol I = 0 I = 1 Description
  AND 0xxx 8xxx AND memory word to AC
  ADD 1xxx 9xxx Add memory word to AC
  LDA 2xxx Axxx Load AC from memory
  STA 3xxx Bxxx Store content of AC into memory
  BUN 4xxx Cxxx Branch unconditionally
  BSA 5xxx Dxxx Branch and save return address
  ISZ 6xxx Exxx Increment and skip if zero
  CLA 7800 Clear AC
  CLE 7400 Clear E
  CMA 7200 Complement AC
  CME 7100 Complement E
  CIR 7080 Circulate right AC and E
  CIL 7040 Circulate left AC and E
  INC 7020 Increment AC
  SPA 7010 Skip next instr. if AC is positive
  SNA 7008 Skip next instr. if AC is negative
  SZA 7004 Skip next instr. if AC is zero
  SZE 7002 Skip next instr. if E is zero
  HLT 7001 Halt computer
  INP F800 Input character to AC
  OUT F400 Output character from AC
  SKI F200 Skip on input flag
  SKO F100 Skip on output flag
  ION F080 Interrupt on
  IOF F040 Interrupt off
Instructions

## Slide 21: INSTRUCTION SET COMPLETENESS
Instruction Types
A computer should have a set of instructions so that the user can construct machine language programs to evaluate any function that is known to be computable.
  Functional Instructions
  - Arithmetic, logic, and shift instructions
  - ADD, CMA, INC, CIR, CIL, AND, CLA
  Transfer Instructions
  - Data transfers between the main memory
  and the processor registers
  - LDA, STA
  Control Instructions
  - Program sequencing and control
  - BUN, BSA, ISZ
  Input/Output Instructions
  - Input and output
  - INP, OUT
Instructions

## Slide 22: CONTROL UNIT
Instruction codes
Control unit (CU) of a processor translates from machine instructions to the control signals for the microoperations that implement them
Control units are implemented in one of two ways:
Hardwired Control
  CU is made up of sequential and combinational circuits to generate the control signals
Microprogrammed Control
  A control memory on the processor contains microprograms that activate the necessary control signals
We will consider a hardwired implementation of the control unit for the Basic Computer

## Slide 23: TIMING AND CONTROL
Control unit of Basic Computer
Timing and control
Instruction register (IR)
15
14 13 12
11 - 0
3 x 8
decoder
7 6 5 4 3 2 1 0
I
D
0
15 14 . . . . 2 1 0
4 x 16
decoder
4-bit
Sequence
Counter
(SC)
Increment (INR)
Clear (CLR)
Clock
Other inputs
Control
signals
D
T
T
7
15
0
Combinational
Control
logic

## Slide 24: TIMING SIGNALS
- Timing signals are generated by a 4-bit sequence counter (SC) and 4X16 decoder
- The SC can be incremented or cleared.
- Example: T0, T1, T2, T3, T4, T0, T1, . . .
Assume: At time T4, SC is cleared to 0 if decoder output D3 is active.
D3T4: SC  0
Timing and control
Decoder output
The positive clock edge labeled by T0 will trigger only those registers whose control inputs are connected to timing signal T0.

## Slide 25: TIMING SIGNALS
It is crucial to understand the relationship between the timing signals and clock transitions.
For example: T0: AR  PC
Specifies a transfer from PC to AR if timing signal T0 is active.
T0 is active during an entire clock cycle interval.
During this interval, the contents in PC is placed on the bus (S2S1S0 = 010) and the LD (load) input of AR is enabled.
The actual transfer does not occur until the end of the clock cycle when the clock goes through a positive transition.
This same positive edge increments SC from 0000 to 0001.
Timing and control

## Slide 26: INSTRUCTION CYCLE
In the Basic Computer, a machine instruction is executed in “an instruction cycle”. This cycle has the following phases:
  Fetch an instruction from memory
  Decode the instruction
  Read the effective address from memory if the instruction has an indirect address
  Execute the instruction
After an instruction is executed, the cycle starts again at step 1, for the next instruction
  Note: Every different processor has its own (different) instruction cycle

## Slide 27: FETCH and DECODE
T0: AR PC (S0S1S2=010, T0=1)
T1: IR  M [AR], PC  PC + 1 (S0S1S2=111, T1=1)
T2: D0, . . . , D7  Decode IR(12-14), AR  IR(0-11), I  IR(15)
S2
S1
S0
Bus
7
Memory
unit
Address
Read
AR
LD
PC
INR
IR
LD
Clock
1
2
5
Common bus
T1
T0
Instruction Cycle

## Slide 28: DETERMINE THE TYPE OF INSTRUCTION
= 0 (direct)
D7' I T3: AR M[AR]
D7' I’ T3: Nothing
D7 I‘ T3: Execute a register-reference instr.
D7 I T3: Execute an input-output instr.
Instruction Cycle
Start
SC 
AR

PC
T0
IR

M[AR],
PC

PC + 1
T1
AR

IR(0-11),
I

IR(15)
Decode Opcode in IR(12-14),
T2
D7
= 0 (Memory-reference)
(Register or I/O) = 1
I
I
Execute
register-reference
instruction
SC

0
Execute
input-output
instruction
SC

0
M[AR]

AR
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute
memory-reference
instruction
SC

0
T4

## Slide 29: DETERMINE THE TYPE OF INSTRUCTION
= 0 (direct)
D7' I T3: AR M[AR]
D7' I’ T3: Nothing
D7 I‘ T3: Execute a register-reference instr.
D7 I T3: Execute an input-output instr.
Instruction Cycle
Start
SC 
AR

PC
T0
IR

M[AR],
PC

PC + 1
T1
AR

IR(0-11),
I

IR(15)
Decode Opcode in IR(12-14),
T2
D7
= 0 (Memory-reference)
(Register or I/O) = 1
I
I
Execute
register-reference
instruction
SC

0
Execute
input-output
instruction
SC

0
M[AR]

AR
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute
memory-reference
instruction
SC

0
T4
15 14
12 11
0
I
Opcode
Address
Memory-Reference Instructions
(OP-code = 000 ~ 110)
Register-Reference Instructions
(OP-code = 111, I = 0)
Input-Output Instructions
(OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 30: REGISTER REFERENCE INSTRUCTIONS
r = D7 IT3 => Register Reference Instruction
Bi = IR(i) , i=0,1,2,...,11
- D7 = 1, I = 0
- Register Ref. Instr. is specified in b0 ~ b11 of IR
- Execution starts with timing signal T3
Instruction Cycle
Register Reference Instructions are identified when
r: SC  0
CLA rB11: AC  0
CLE rB10: E  0
CMA rB9: AC  AC’
CME rB8: E  E’
CIR rB7: AC  shr AC, AC(15)  E, E  AC(0)
CIL rB6: AC  shl AC, AC(0)  E, E  AC(15)
INC rB5: AC  AC + 1
SPA rB4: if (AC(15) = 0) then (PC  PC+1)
SNA rB3: if (AC(15) = 1) then (PC  PC+1)
SZA rB2: if (AC = 0) then (PC  PC+1)
SZE rB1: if (E = 0) then (PC  PC+1)
HLT rB0: S  0 (S is the start-stop flip-flop)
Notes: SPA: skip next instruction if AC positive; SNA: negative; SZA: AC zero

## Slide 31: MEMORY REFERENCE INSTRUCTIONS
AND to AC
D0T4: DR  M[AR] Read operand
D0T5: AC  AC  DR, SC  0 AND with AC
ADD to AC
D1T4: DR  M[AR] Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 Add to AC and store carry in E
- The effective address of the instruction is in AR and was placed there during
timing signal T2 when I = 0, or during timing signal T3 when I = 1
- Memory cycle is assumed to be short enough to complete in a CPU cycle
- The execution of MR instruction starts with T4
MR Instructions
Symbol
Operation
Decoder
Symbolic Description
AND D0 AC  AC  M[AR]
ADD D1 AC  AC + M[AR], E  Cout
LDA D2 AC  M[AR]
STA D3 M[AR]  AC
BUN D4 PC  AR
BSA D5 M[AR]  PC, PC  AR + 1
ISZ D6 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1
Notes: BSA: branch and save return address
ISZ: increment and skip if zero

## Slide 32: MEMORY REFERENCE INSTRUCTIONS
LDA: Load to AC
D2T4: DR  M[AR]
D2T5: AC  DR, SC  0
STA: Store AC
D3T4: M[AR]  AC, SC  0
BUN: Branch Unconditionally
D4T4: PC  AR, SC  0

## Slide 33: MEMORY REFERENCE INSTRUCTIONS
MR Instructions
Branch and save return address instruction is useful for branching to
a subroutine or procedure. When the subroutine is executed, the program
returns back to the branching point.
BSA:
D5T4: M[AR]  PC, AR  AR + 1
D5T5: PC  AR, SC  0
Memory, PC after execution
21
0
BSA
135
Next instruction
Subroutine
20
PC = 21
AR = 135
136
1
BUN
135
Memory, PC, AR at time T4
0
BSA
135
Next instruction
Subroutine
20
21
135
PC = 136
1
BUN
135
Memory
Memory

## Slide 34: MEMORY REFERENCE INSTRUCTIONS
MR Instructions
ISZ: Increment and Skip-if-Zero
Increments the word specified by the effective address, and if the incremented value is equal to zero, PC is incremented by 1.
Usually a negative number (in 2’s complement form) is stored in memory. When the number reaches zero, PC is incremented by one, skipping the next instruction.
D6T4: DR ← M[AR]
D6T5: DR ← DR + 1
D6T4: M[AR] ← DR, if (DR = 0) then (PC ← PC + 1), SC ← 0

## Slide 35: FLOWCHART FOR MEMORY REFERENCE INSTRUCTIONS
MR Instructions
Memory-reference instruction
DR  M[AR]
DR  M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC DR
SC  0
AC  AC + DR
E  Cout
SC  0
AC  DR
SC  0
D T
0
4
D T
1
4
D T
2
4
D T
3
4
D T
0
5
D T
1
5
D T
2
5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D T
4
4
D T
5
4
D T
6
4
DR  DR + 1
D T
5
5
D T
6
5
PC  AR
SC  0
M[AR]  DR
If (DR = 0)
then (PC  PC + 1)
SC  0
D T
6
6


## Slide 36: INPUT-OUTPUT AND INTERRUPT
- The terminal sends and receives serial information
- The serial info. from the keyboard is shifted into INPR
- The serial info. for the printer is stored in the OUTR
- INPR and OUTR communicate with the terminal serially and with the AC in parallel.
- The flags are needed to synchronize the timing difference between I/O device and the computer
A Terminal with a keyboard and a Printer
INPR Input register - 8 bits
OUTR Output register - 8 bits
FGI Input flag - 1 bit
FGO Output flag - 1 bit
IEN Interrupt enable - 1 bit
I/O and Interrupt
Input-Output Configuration
Input-output
terminal
Serial
communication
interface
Computer
registers and
flip-flops
Printer
Keyboard
Receiver
interface
Transmitter
interface
FGO
OUTR
AC
INPR
FGI
Serial Communications Path
Parallel Communications Path

## Slide 37: PROGRAM CONTROLLED DATA TRANSFER
INPUT:
Initially, the input flag FGI is cleared to 0.
When a key is struck, the 8-bit code of the key is shifted into INPR and FGI is set to 1.
As long as FGI=1, the content of INPR cannot be changed by pressing another key.
The computer checks FGI, if FGI=1, AC  INPR and FGI  0.
OUTPUT:
Initially, the output flag FGO is set to 1.
The computer checks FGO, if FGO=1 then OUTR AC and FGO  0
The output device (e.g. printer) accepts the content of OUTR and set FGO to 1.
While FGO=0, the computer does not load a new character to FGO because FGO=0 indicates that the output device is busy.
I/O and Interrupt

## Slide 38: PROGRAM CONTROLLED DATA TRANSFER
loop: If FGI = 1 goto loop
INPR  new data, FGI  1
loop: If FGO = 1 goto loop
consume OUTR, FGO  1
-- CPU -- -- I/O Device --
/* Input */ /* Initially FGI = 0 */
loop: If FGI = 0 goto loop
AC  INPR, FGI  0
/* Output */ /* Initially FGO = 1 */
loop: If FGO = 0 goto loop
OUTR  AC, FGO  0
I/O and Interrupt
Start Input
FGI  0
FGI=0
AC  INPR
More
Character
END
Start Output
FGO  0
FGO=0
More
Character
END
OUTR  AC
AC  Data
yes
no
yes
no
FGI=0
FGO=1
yes
yes
no
no
Flowchart summary of the previous slide:

## Slide 39: INPUT-OUTPUT INSTRUCTIONS
D7IT3 = p (used as a logic variable below)
IR(i) = Bi, i = 6, …, 11
p: SC  0 Clear SC
INP pB11: AC(0-7)  INPR, FGI  0 Input char. to AC
OUT pB10: OUTR  AC(0-7), FGO  0 Output char. from AC
SKI pB9: if(FGI = 1) then (PC  PC + 1) Skip on input flag
SKO pB8: if(FGO = 1) then (PC  PC + 1) Skip on output flag
ION pB7: IEN  1 Interrupt enable on
IOF pB6: IEN  0 Interrupt enable off
In an I/O instruction’s code, the most significant 4 bits is 1111.

## Slide 40: PROGRAM-CONTROLLED INPUT/OUTPUT
Program-controlled I/O
- Continuous CPU involvement (see below)
I/O takes valuable CPU time
- CPU slowed down to I/O speed
- Simple
- Minimal hardware
I/O and Interrupt
Input
LOOP, SKI DEV
BUN LOOP
INP DEV
Output
LOP, LDA DATA
LOOP, SKO DEV
BUN LOOP
OUT DEV
Alternative solution is interrupt initiated I/O

## Slide 41: INTERRUPT INITIATED INPUT/OUTPUT
- Open communication only when some data has to be passed --> interrupt.
- The I/O interface, instead of the CPU, monitors the I/O device.
- When the interface founds that the I/O device is ready for data transfer,
it generates an interrupt request to the CPU
Upon detecting an interrupt, the CPU
  stops momentarily the task it is doing,
  branches to the service routine to process the data transfer, and then
  returns to the task it was performing.
* IEN (Interrupt-enable flip-flop)
- can be set and cleared by instructions
- when cleared, the computer cannot be interrupted

## Slide 42: FLOWCHART FOR INTERRUPT CYCLE
R = Interrupt f/f
The interrupt cycle is a HW implementation of a branch and save return address operation.
At the beginning of the next instruction cycle, the instruction that is read from memory is in address 1.
At memory address 1, the programmer must store a branch instruction that sends the control to an interrupt service routine
The instruction that returns the control to the original program is "indirect BUN 0"
I/O and Interrupt
Store return address
R
=1
=0
in location 0
M[0]  PC
Branch to location 1
PC  1
IEN  0
R  0
Interrupt cycle
Instruction cycle
Fetch and decode
instructions
IEN
FGI
FGO
Execute
instructions
R  1
=1
=1
=1
=0
=0
=0

## Slide 43: REGISTER TRANSFER OPERATIONS IN INTERRUPT CYCLE
Register Transfer Statements for Interrupt Cycle
- R F/F  1 if IEN (FGI + FGO)T0T1T2
 T0T1T2 (IEN)(FGI + FGO): R  1
- The fetch and decode phases of the instruction cycle
must be modified Replace T0, T1, T2 with R'T0, R'T1, R'T2
- The interrupt cycle :
RT0: AR  0, TR  PC
RT1: M[AR]  TR, PC  0
RT2: PC  PC + 1, IEN  0, R  0, SC  0
After interrupt cycle
0
BUN
1120
0
1
PC = 256
255
1
BUN
0
Before interrupt
Main
Program
1120
I/O
Program
0
BUN
1120
0
PC = 1
256
255
1
BUN
0
Memory
Main
Program
1120
I/O
Program
256
I/O and Interrupt
At the end of the I/O program IEN1 so that further interrupts are enabled.

## Slide 44: FURTHER QUESTIONS ON INTERRUPT
  How can the CPU recognize the device
  requesting an interrupt ?
  Since different devices are likely to require
  different interrupt service routines, how can
  the CPU obtain the starting address of the
  appropriate routine in each case ?
  Should any device be allowed to interrupt the
  CPU while another interrupt is being serviced ?
  How can the situation be handled when two or
  more interrupt requests occur simultaneously ?
I/O and Interrupt

## Slide 45: FLOWCHART FOR INTERRUPT CYCLE
I/O and Interrupt
R = Interrupt f/f
Store return address
R
=1
=0
in location 0
M[0]  PC
Branch to location 1
PC  1
IEN  0
R  0
Interrupt cycle
Instruction cycle
Fetch and decode
instructions
IEN
FGI
FGO
Execute
instructions
R  1
=1
=1
=1
=0
=0
=0
After interrupt cycle
0
BUN
1120
0
1
PC = 256
255
1
BUN
0
Before interrupt
Main
Program
1120
I/O
Program
0
BUN
1120
0
PC = 1
256
255
1
BUN
0
Memory
Main
Program
1120
I/O
Program
256

## Slide 46: FETCH and DECODE
= 0 (direct)
Instrction Cycle
Start
SC 
AR

PC
T0
IR

M[AR],
PC

PC + 1
T1
AR

IR(0-11),
I

IR(15)
Decode Opcode in IR(12-14),
T2
D7
= 0 (Memory-reference)
(Register or I/O) = 1
I
I
Execute
register-reference
instruction
SC

0
Execute
input-output
instruction
SC

0
M[AR]

AR
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute
memory-reference
instruction
SC

0
T4

## Slide 47: COMPLETE COMPUTER DESCRIPTION Flowchart of Operations
Description
=1 (I/O) =0 (Register) =1 (Indir) =0 (Dir)
start
SC  0, IEN  0, R  0
R
AR  PC
R’T0
IR  M[AR], PC  PC + 1
R’T1
AR  IR (0~11), I  IR (15)
D0...D7  Decode IR (12~14)
R’T2
AR  0, TR  PC
RT0
M[AR]  TR, PC  0
RT1
PC  PC + 1, IEN  0
R  0, SC  0
RT2
D7
I
I
Execute
I/O
Instruction
Execute
RR
Instruction
AR  M[AR]
Idle
D7IT3 D7I’T3
D7’IT3 D7’I’T3
Execute MR
Instruction
=0 (Instruction =1 (Interrupt
Cycle) Cycle)
=1 (Register or I/O) =0 (Memory Ref)
D7’T4

## Slide 48: COMPLETE COMPUTER DESCRIPTION Microoperations
Description
Fetch
Decode
Indirect
Interrupt
Memory-Reference
AND
ADD
LDA
STA
BUN
BSA
ISZ
R’T0 :
R’T1 :
R'T2 :
D7’IT 3:
RT0 :
RT1 :
RT2 :
D0T4 :
D0T5 :
D1T4 :
D1T5 :
D2T4 :
D2T5 :
D3T4 :
D4T4 :
D5T4 :
D5T5 :
D6T4 :
D6T5 :
D6T6 :
AR  PC
IR  M[AR], PC  PC + 1
D0, ..., D7  Decode IR (12~14),
AR  IR (0~11), I  IR (15)
AR  M[AR]
R  1
AR  0, TR  PC
M[AR]  TR, PC  0
PC  PC + 1, IEN  0, R  0, SC  0
DR  M[AR]
AC  ACDR, SC  0
DR  M[AR]
AC  AC + DR, E  Cout, SC  0
DR  M[AR]
AC  DR, SC  0
M[AR]  AC, SC  0
PC  AR, SC  0
M[AR]  PC, AR  AR + 1
PC  AR, SC  0
DR  M[AR]
DR  DR + 1
M[AR]  DR, if (DR=0) then (PC  PC + 1),
SC  0
T0’T1’T2’(IEN)(FGI + FGO) :

## Slide 49: COMPLETE COMPUTER DESCRIPTION Microoperations
D7I’T3 = r
IR (i) = Bi
r :
rB11 :
rB10 :
rB9 :
rB8 :
rB7 :
rB6 :
rB5 :
rB4 :
rB3 :
rB2 :
rB1 :
rB0 :
D7IT3 = p
IR (i) = Bi
p :
pB11 :
pB10 :
pB9 :
pB8 :
pB7 :
pB6 :
Description
Register-Reference
CLA
CLE
CMA
CME
CIR
CIL
INC
SPA
SNA
SZA
SZE
HLT
Input-Output
INP
OUT
SKI
SKO
ION
IOF
(Common to all register-reference instructions)
(i = 0,1,2, ..., 11)
SC  0
AC  0
E  0
AC  AC’
E  E’
AC  shr AC, AC(15)  E, E  AC(0)
AC  shl AC, AC(0)  E, E  AC(15)
AC  AC + 1
If (AC (15) =0) then (PC  PC + 1)
If (AC (15) =1) then (PC  PC + 1)
If (AC = 0) then (PC  PC + 1)
If (E=0) then (PC  PC + 1)
S  0
(Common to all input-output instructions)
(i = 6,7,8,9,10,11)
SC  0
AC (0-7)  INPR, FGI  0
OUTR  AC (0-7), FGO  0
If (FGI=1) then (PC  PC + 1)
If (FGO=1) then (PC  PC + 1)
IEN  1
IEN  0

## Slide 50: DESIGN OF BASIC COMPUTER(BC)
Hardware Components of BC
A memory unit: 4096 x 16.
Registers:
AR, PC, DR, AC, IR, TR, OUTR, INPR, and SC
Flip-Flops(Status):
I, S, E, R, IEN, FGI, and FGO
Decoders: a 3x8 Opcode decoder
a 4x16 timing decoder
Common bus: 16 bits
Control logic gates:
Adder and Logic circuit: Connected to AC
Control Logic Gates
  - Input Controls of the nine registers
  - Read and Write Controls of memory
  - Set, Clear, or Complement Controls of the flip-flops
  - S2, S1, S0 Controls to select a register for the bus
  - AC, and Adder and Logic circuit
Design of Basic Computer

## Slide 51: CONTROL OF REGISTERS AND MEMORY
Scan all of the register transfer statements that change the content of AR:
LD(AR) = R'T0 + R'T2 + D'7IT3
CLR(AR) = RT0
INR(AR) = D5T4
Address Register; AR
R’T0: AR  PC LD(AR)
R’T2: AR  IR(0-11) LD(AR)
D’7IT3: AR  M[AR] LD(AR)
RT0: AR  0 CLR(AR)
D5T4: AR  AR + 1 INR(AR)
Design of Basic Computer
AR
LD
INR
CLR
Clock
To bus
12
From bus
12
D'
I
T
T
R
T
D
T
7
3
2
0
4

## Slide 52: CONTROL OF FLAGS
ION = pB7: IEN  1 (I/O Instruction)
IOF = pB6: IEN  0 (I/O Instruction)
RT2: IEN  0 (Interrupt)
p = D7IT3 (Input/Output Instruction)
IEN: Interrupt Enable Flag
Design of Basic Computer
D
I
T3
7
J
K
Q
IEN
p
B
7
B
6
T
2
R

## Slide 53: CONTROL OF THE COMMON BUS
For AR
D4T4: PC  AR
D5T5: PC  AR
x1 = D4T4 + D5T5
Design of Basic Computer
x1
x2
x3
x4
x5
x6
x7
Encoder
S
2
S
1
S
0
Multiplexer
bus select
inputs
x1 x2 x3 x4 x5 x6 x7
S2 S1 S0
selected
register
0 0 0 0 0 0 0 0 0 0 none
1 0 0 0 0 0 0 0 0 1 AR
0 1 0 0 0 0 0 0 1 0 PC
0 0 1 0 0 0 0 0 1 1 DR
0 0 0 1 0 0 0 1 0 0 AC
0 0 0 0 1 0 0 1 0 1 IR
0 0 0 0 0 1 0 1 1 0 TR
0 0 0 0 0 0 1 1 1 1 Memory

## Slide 54: CONTROL OF THE AC REGISTER AND THE DESIGN OF ACCUMULATOR LOGIC
All the statements that change the content of AC
Design of AC Logic
Circuits associated with AC
16
16
8
Adder and
logic
circuit
16
AC
From DR
From INPR
Control
gates
LD
INR
CLR
16
To bus
Clock
D0T5: AC  AC  DR AND with DR
D1T5: AC  AC + DR Add with DR
D2T5: AC  DR Transfer from DR
pB11: AC(0-7)  INPR Transfer from INPR
rB9: AC  AC Complement
rB7 : AC  shr AC, AC(15)  E Shift right
rB6 : AC  shl AC, AC(0)  E Shift left
rB11 : AC  0 Clear
rB5 : AC  AC + 1 Increment
r=D7I’T3
p=D7IT3

## Slide 55: CONTROL OF AC REGISTER
Gate structures for controlling
the LD, INR, and CLR of AC
AC
LD
INR
CLR
Clock
To bus
16
From Adder
and Logic
16
AND
ADD
DR
INPR
COM
SHR
SHL
INC
CLR
D
0
D
1
D
2
B
11
B
9
B
7
B
6
B
5
B
11
r
p
T
5
T
5
Design of AC Logic

## Slide 56: ALU (ADDER AND LOGIC CIRCUIT)
One stage of Adder and Logic circuit
Design of AC Logic
AND
ADD
DR
INPR
COM
SHR
SHL
J
K
Q
AC(i)
LD
FA
C
C
From
INPR
bit(i)
DR(i)
AC(i)
AC(i+1)
AC(i-1)
i
i
i+1
I

## Slide 57: A sample program (for the Basic Computer)

## Slide 58: A sample program (for the Basic Computer)
Binary machine code
Same program in HEX code

## Slide 59: A sample program (for the Basic Computer)
Same program from previous slide, with symbolic operation codes
What does this program do?

## Slide 60: A sample program (for the Basic Computer)
Same program from previous slide in Assembly Language
The “assembler” translates this program to binary machine code.

## Slide 61: Program to demonstrate loops
int i, a=0;
for(i=0 ; i<5 ; i++) a++;
ORG 100
LDA LIM
STA VRI
LOP, ISZ VRA
ISZ VRI
BUN LOP
HLT
VRA, DEC 0
VRI, DEC 0
LIM, DEC -5